## Slide 1: From CAD drawings to a checked BOQ — automatically
How the Static Group QTO prototype works, explained simply · Mr. Ramzi Villa
Notes: Purpose: explain in plain terms what the prototype automates and why it matters.

## Slide 2: Today, quantities are measured by hand
1
Open every drawing
Plans, schedules, sections — spread across many sheets
2
Find each element
Footings, columns, beams, slabs, walls
3
Read the sizes
Length and width on plans; depth and thickness on other sheets
4
Calculate in Excel
L × W × D for hundreds of items
5
Check against the BOQ
Line by line, then chase every difference
The cost
Days of work per project
Easy to miss or double-count items
Hard to prove where a number came from
Errors in the drawings often go unnoticed
Every drawing revision means starting again

## Slide 3: The system does the measuring; the engineer reviews
1
Read
Opens every DXF file of the project
2
Identify
Finds footings, columns, beams, slabs, walls from CAD layers and tags
3
Measure
Takes exact sizes from the drawn geometry
4
Look up
Reads thickness and depth from the consultant's own schedules
5
Calculate
Computes every volume with a visible formula
6
Compare
Builds the BOQ and checks it against the client's BOQ
7
Flag
Sends anything missing or inconsistent to a review queue
Steps 1–6 are automatic. The engineer only works on step 7 — the items the system could not confirm.

## Slide 4: Proven on the real villa drawings
80
DXF drawings read
0 failed
247
construction elements
identified automatically
426 m³
concrete calculated
+ 25.7 m³ blinding
175
BOQ lines generated
each traceable to the drawing
Footing sizes match the earlier Excel prototype exactly — and 3 items Excel could not identify are now identified (CF1 and two rafts).
27 elements were left without a quantity on purpose: the drawings do not give a value, so the system flags them instead of guessing.

## Slide 5: Every number shows where it came from
Example: footing F3
Drawing
S-FP.dxf (foundation plan)
CAD layer
S-FNDN-FTNG
Length × width
2.600 × 2.200 m — measured from the outline
Depth
450 mm — footing schedule on S-FD.dxf
Cross-check
Drawn size = schedule size ✔
Calculation
2.600 × 2.200 × 0.450
= 2.574 m³
Click any quantity in the app to see this evidence, with the element highlighted on the drawing. Anyone — engineer, QS or client — can check it in seconds.

## Slide 6: It also catches mistakes in the drawings
!
Column C7 · Ground floor
Drawn 300 × 600 mm
Schedule says 250 × 600 mm
!
Column C16 · First floor
Drawn 200 × 600 mm
Schedule says 200 × 700 mm
!
Beams PHB7 & PHB8 · Penthouse
Drawn 200 mm wide
Schedule says 300 mm wide
Real inconsistencies between the consultant's plans and schedules, found by automatic cross-checking. Raised before construction, they cost a phone call; found on site, they cost rework.

## Slide 7: What changes for the team
Before
With the system
QS measures every item by hand
Days per project
Numbers live in personal spreadsheets
Drawing errors found late
Revision = start again
System measures; QS reviews flagged items
Minutes to process a full drawing set
Every number linked to its drawing source
Plan vs schedule conflicts flagged early
Revision = re-run and compare

## Slide 8: What still needs a person — by design
1
No real BOQ yet
The comparison was demonstrated with a clearly labelled test BOQ. It must now be run on a real one.
2
Storey heights
Not drawn as numbers; derived from level tags and must be confirmed by an engineer.
3
Incomplete drawings
Some slab zones and beams have no thickness or depth on the drawings; they stay flagged, never guessed.

## Slide 9: Next step: prove it on a real BOQ
Run it on a past project that has drawings + BOQ · time the QS review against manual take-off · then add formwork and rebar